This slide deck is still under construction (July 15, 2016)
Formal Specification of Bluespec BSV's
Static Elaboration and Dynamic Semantics
Rishiyur S. Nikhil
July 2016
www.bluespec.com
© Bluespec, Inc., 2016

---
Introduction
Bluespec BSV is a High Level Hardware Description Language (HLHDL):
Haskell
for type system and static elaboration (programmatic circuit structural description)
Guarded Atomic Actions (Rewrite Rules)
for abstract functional behavior (“untimed”)
Schedule Semantics
for timed behavior (with clocks)
BSV programs are compiled in stages into silicon:
FPGA
synthesis,
P&R, etc.
FPGA
bitfile
BSV
program
bsc
compiler
Verilog
program
ASIC
synthesis,
P&R, etc.
ASIC
This work is about describing BSV semantics directly (implementation-independent):
Abstract operational semantics, given as a Haskell program on BSV syntax
For what purpose?
Pedagogy: teaching BSV to new users (students, engineers, …)
Reference model for BlueCheck formal checking (QuickCheck in BSV)
Future: proofs of correctness

---
Introduction (contd.)
Bluespec BSV is a High Level Hardware Description Language (HLHDL):
Haskell
for type system and static elaboration (programmatic circuit structural description)
Guarded Atomic Actions (Rewrite Rules)
for abstract functional behavior (“untimed”)
Schedule Semantics
for timed behavior (with clocks)
This talk: outline of the issues and ideas behind Schedule Semantics
The Haskell code, a detailed document, and these slides available at:
https://github.com/rsnikhil/Bluespec_BSV_Formal_Semantics

---
Motivating example: packet credit counter
module m2
module m1
Network
Fabric
consume
packets
produce
packets
send
decr
incr
credit
counter
credit
counter
incr
decr
produce
packets
consume
packets
send
Purpose: flow control to avoid having to drop packets
The value of a credit counter = guaranteed available space in the remote receive-buffer
Decrement credits when you send a packet
Increment credits when credits are returned on received packets

---
A BSV implementation of the credit counter
interface Counter_IFC;
   method ActionValue #(Int #(32)) count1 (Int #(32) delta);
   method ActionValue #(Int #(32)) count2 (Int #(32) delta);
   method Int #(32) query_credit;
endinterface
module mkCounter (Counter_IFC);
   Reg #(Int #(32)) rg <- mkReg (0);
   method ActionValue #(Int #(32)) count1 (Int #(32) delta);
      rg <= rg + delta;
      return rg;
   endmethod
   method ActionValue #(Int #(32)) count2 (Int #(32) delta);
      rg <= rg + delta;
      return rg;
   endmethod
   method Int #(32) query_credit;
      return rg;
   endmethod
endmodule
Notes:
Int #(32)	The type of a signed 32-bit integer
Reg #(t)	The interface type of a register holding a value of type t,
with methods _read( ) and _write (v)
ActionValue #(t)	Monadic type; when invoked, has some side effect, returns a value of type t
< - mkReg (0)	Monadic instantiation (allocation) of a register module with reset value 0
rg <= rg + delta	Syntactic sugar for: rg._write (rg._read + delta)

---
Motivating example: sketch of module m1's code
module mkM1 (M1_IFC);
   Counter_IFC counter ← mkCounter;
   … other local state instantiations … ;
   rule send (… rule condition …);
      let c1 ← counter.count1 (+1);
      …
   endrule
   rule consume_packets (… rule condition …);
      let c2 ← counter.count2 (-1);
      …
   endrule
   … other rules … counter.query_credit …
   … this modules interface method defs …
endmodule
module m1
produce
packets
send
decr
credit
counter
incr
consume
packets
Expressions are built out of constants, primitive functions and method calls
Method and rule conditions are expressions of type Bool
Rule bodies are expressions of type Action
Method bodies are expressions of type Action, ActionValue #(t) or any other value type t

---
The issue: how to map rules into clocks?
module mkM1 (M1_IFC);
   Counter_IFC counter ← mkCounter;
   … other local state instantiations … ;
   rule send (… rule condition …);
      let c1 ← counter.count1 (+1);
      …
   endrule
   rule consume_packets (… rule condition …);
      let c2 ← counter.count2 (-1);
      …
   endrule
   … other rules … counter.query_credit …
   … this modules interface method defs …
endmodule
module m1
produce
packets
send
decr
credit
counter
incr
consume
packets
We'd like to capture hardware constraints abstractly. E.g.,:
Rules send and consume_packets cannot both execute in the same clock, because:
They call methods counter.count1 and counter.count2 which both write register rg inside the counter module.
In clocked hardware, a register can be written at most once in a clock.
On the other hand, can one of those rules execute in the same clock as a rule calling the query_credit method?
If so, what value does query_credit return: pre-increment or post-increment?

---
The issue: how to map rules into clocks?
module mkM1 (M1_IFC);
   Counter_IFC counter ← mkCounter;
   … other local state instantiations … ;
   rule send (… rule condition …);
      let c1 ← counter.count1 (+1);
      …
   endrule
   rule consume_packets (… rule condition …);
      let c2 ← counter.count2 (-1);
      …
   endrule
   … other rules … counter.query_credit …
   … this modules interface method defs …
endmodule
module m1
produce
packets
send
decr
credit
counter
incr
consume
packets
Puzzle: what if we want want rules send and consume_packets to execute in the same clock for better performance?
We'll need a primitive that can “accept two writes in a clock” (not just an ordinary register).
What does this mean, and how do we capture the idea abstractly?

---
Rule semantics: overview
Rule semantics are explained in two parts:
Individual rule: logically, a rule fires in a single instant. All the Actions in the rule (and any methods it calls) happen at the same instant. We call this Action parallelism.
Multiple rules within a clock: logically, they execute in sequence, so the overall state change in a clock can be understood as the simple sequential composition of the state changes of the individual rules. We call this Rule parallelism or concurrency.
Visualization:
1. Action Parallelism: all the Actions ( ) in a Rule occur at the same instant ( | )
2. Rule Parallelism (Concurrency)
Rule
execution
(logical view)
Clocks

---
Single rule semantics (Action Parallelism)
Every rule can be regarded as a flow of data from constants and outputs of methods, through functions and operators, ending in inputs to Action methods (this flow is always a combinational circuit, a pure function).
rule compute ((y != 0) && got_x && got_y) ;
   if (lsb(y) == 1) w <= w + x;
   x <= x << 1;
   y <= y >> 1;
endrule
Example: below is a visualization of the flow for the rule shown at right
w._read( )
got_y._read( )
y._read( )
got_x._read( )
x._read( )
0
lsb
&&
!=
1
1
1
&&
>>
<<
==
+
CAN_FIRE
&&
enable
enable
enable
w._write( )
y._write( )
x._write( )
Actions
All these actions are performed at the same instant.

---
Abstract characterization of primitives
All primitives are characterized in a uniform, abstract manner
which, in turn, imply constraints on rule parallelism.
Each primitive with methods m1, m2, …, mN in its interface
is characterized by three sets of properties:
The state will of course be different for different primitives.
E.g., for registers:
f (_write, x, y) → (y, void)
f (_read, x) → x
Functions capturing the functionality of each method:
f (mi, state, args, …) → (state, result)
Whether or not these two methods can be called in the same action. E.g., for registers
f_ap (_write, _write) → False
f_ap (_read, _write) → True
For every pair of methods, an Action Parallelism constraint:
f_ap (mi, mj) → Bool
Whether or not these two methods can be called in two rules in that order. E.g., for registers
f_rp (_write, _write) → False
f_rp (_read, _write) → True
f_rp (_write, _read) → False
f_rp (_read, _read) → True
For every pair of methods, a Rule Parallelism constraint:
f_rp (mi, mj) → Bool

---
Universal (“hardware”) constraints
For every pair of methods, an Action Parallelism constraint:
f_ap (mi, mj) → Bool
f_ap (mj, mj) → False
if mj has type Action, ActionValue #(t) or has >0 arguments
For every pair of methods, a Rule Parallelism constraint:
f_rp (mi, mj) → Bool
f_ap (mj, mj) → False
if mj has type Action, ActionValue #(t) or has >0 arguments

---
Rule Parallelism (multiple rules in a clock)
Define a schedule as a list of rules to be executed in a clock:
Then, the semantics of multiple rules in a clock (rule parallelism) is simple:
For each clock:
Consider each rule in the schedule in order
        If rJ does not conflict with earlier rules (r1..rJ-1)
        Execute rJ according to the per-rule semantics
        (i.e., if its CAN_FIRE is true, do its actions)
Conflict:
f_ap or f_rp is False
In grey: rule that does not fire; either conflicts with earlier rule, or CAN_FIRE is False
In red: rule that fires
Rule
execution
(logical view)
r1 r2 rN
r1 r2 rN
r1 r2 rN
Clocks
r1 r2 rN
r1 r2 rN

---
The semantics expressed as a Haskell program
All these concepts have been coded as a Haskell program
that represents the formal abstract operational semantics of BSV:
        https://github.com/rsnikhil/Bluespec_BSV_Formal_Semantics
Inputs:
A BSV program
A table of characterization-functions for primitives (no “built-in” primitive)
A scheduling function
(instead of a list, a function to pick the next rule to consider in this clock)
Parses the BSV program
Performs “static elaboration”: this is just classical Haskell execution whose output is the circuit described by the BSV program (hierarchy of module instances).
Executes the BSV program according to the given schedule and primitives,
rule by rule and clock by clock, so that the state is available at each step.

---
Relationship to the current bsc compiler
The semantics described here is more general than what is implemented by the bsc compiler.
The bsc compiler does the same static elaboration
The bsc compiler pre-computes a fixed static schedule based on static analysis of the rules in the program
It tries to maximize rule concurrency based on method ordering constraints
It generates circuits to suppress a rule dynamically if it conflicts with earlier rules

---
Using this semantic formalization
The initial purpose of this formalization was pedagogy:
Teaching new users (students, engineers), giving them a simple mental model to understand BSV semantics.
The next use is likely to be in BlueCheck (QuickCheck in BSV):
BlueCheck
Haskell
model
BSV
program
schedule
BlueSim
or Verilog
simulation
bsc
compiler
Future: formal reasoning about BSV:
Correctness of refinements
Correctness of composition
Correctness of bsc compiler
…

---
Returning to our puzzle
module mkM1 (M1_IFC);
   Counter_IFC counter ← mkCounter;
   … other local state instantiations … ;
   rule send (… rule condition …);
      let c1 ← counter.count1 (+1);
      …
   endrule
   rule consume_packets (… rule condition …);
      let c2 ← counter.count2 (-1);
      …
   endrule
   … other rules … counter.query_credit …
   … this modules interface method defs …
endmodule
module m1
produce
packets
send
decr
credit
counter
incr
consume
packets
Puzzle: what if we want want rules send and consume_packets to execute in the same clock for better performance?
We'll need a primitive that can “accept two writes in a clock” (not just an ordinary register).
What does this mean, and how do we capture the idea abstractly?

---
CRegs (Concurrent Registers)
A CReg provides a vector of standard Reg interfaces that can be operated concurrently:
interface CReg #(numeric type n, type t);
   interface Vector #(n, Reg #(t)) ports;
endinterface
Method ordering constraints for CReg:
This is the same as the standard register method-ordering constraint
ports [0]._read <= ports [0]._write <
ports[1]._read <= ports[1]._write <
ports[2]._read <= ports[2]._write <
… …
ports[n-1]._read <= ports[n-1]._write
But note that a value written in port 0 can be read concurrently on port 1 (by a logically later rule in the same clock), unlike an ordinary register where a write can only be read in the next clock

---
A possible implementation of a CReg
This figure shows a possible circuit implementation of a CReg:
write[0]
CReg
write[1]
write[n-1]
read[0]
read[1]
read[n-1]
But note, this is not a definition of an CReg, it is merely shown to strengthen intuition. It is important, as usual, to keep separate the logical semantics from any implementation semantics. When using CRegs in BSV, one only needs to consider its method-ordering constraints (shown in the previous slide).
Internal register
data
EN
data
EN
data
EN

---
mkCounter again, but with greater concurrency
module mkCounter (Counter_IFC);
   Reg #(Int #(32)) rg <- mkReg (0);
   method ActionValue #(Int #(32)) count1 (Int #(32) delta);
      rg <= rg + delta;
      return rg;
   endmethod
   method ActionValue #(Int #(32)) count2 (Int #(32) delta);
      rg <= rg + delta;
      return rg;
   endmethod
endmodule
module mkCounter (Counter_IFC);
   Array #(Reg #(Int #(32))) rg <- mkCReg (2, 0);
   method ActionValue #(Int #(32)) count1 (Int #(32) delta);
      rg[0] <= rg[0] + delta;
      return rg[0];
   endmethod
   method ActionValue #(Int #(32)) count2 (Int #(32) delta);
      rg[1] <= rg[1] + delta;
      return rg[1];
   endmethod
endmodule

---
mkCounter again, but with greater concurrency
Reg version:
CAN_FIRE_rl_2 is true, but WILL_FIRE_rl_2 is false as long as WILL_FIRE_rl_1 is true, because of the conflict on methods count1 and count2
Picture file: Waves_CReg.tiff
CReg version:
CAN_FIRE_rl_2 is true, and WILL_FIRE_rl_2 is also true even though WILL_FIRE_rl_1 is true, because of there the methods count1 and count2 do not conflict.

---
End

---
Method Ordering Constraints (inducing conflicts)
Consider two rules rule1 and rule2, in that order.
Consider two method calls x.mA in rule1, and x.mB in rule2, on a common module x. These methods can be either in the condition or body or rule1 and rule2.
For every module (x), we know certain ordering constraints on its methods:
Constraint	Meaning
mA conflict_free mB	Rules invoking mA and mB can fire concurrently (either order)
mA < mB	Rules invoking mA and mB can fire concurrently, provided the rule invoking mA is earlier than the rule invoking mB
mB < mA	Rules invoking mA and mB can fire concurrently, provided the rule invoking mB is earlier than the rule invoking mA
mA conflict mB	Rules invoking mA and mB cannot fire concurrently (neither order)
For primitive modules the ordering constraints on its interface methods are built-in (“given”).
For a user-defined module, the ordering constraints on its interface methods can be systematically inferred from the module definition.
rule1
x.mA
rule2
x.mB

---
Example: method ordering constraints on registers
For the mkReg register primitive, a method ordering constraint is: _read < _write
(One can see that this maps easily into hardware: during a clock, we can only read the old value (from the last clock edge) and when we write, it is only visible after the next clock edge.)
These constraints may result in a conflict for some rule schedules.
No conflict: rule order is consistent with method ordering constraint (and maps naturally to HW semantics)
Conflict: rule order is inconsistent with method ordering constraint
rule1
rule2
rule2
rule1
x._read
x._write
x._write
x._read
Rules
Rules
Clocks
Clocks

---
Example: method ordering constraints on FIFOs
The mkPipelineFIFO primitive has this method ordering constraint:
        {deq, first} < enq
No conflict: rule order is consistent with method ordering constraint
Conflict: rule order is inconsistent with method ordering constraint
rule1
rule2
rule2
rule1
x.deq
x.enq
x.enq
x.first
Rules
Rules
Clocks
Clocks

---
From method ordering to rule ordering
In the past few slides, we have focused on some particular pair of methods in two rules that are arranged in some particular order.
Of course, rules typically invoke several methods, often on several sub-modules.
We say that there is a conflict between an ordered pair of rules r1 and r2
if there is a conflict between any pair of methods x.m1 in r1 and x.m2 in r2.
r1
r2
conflict?
x.m1
x.m2
x.m3
z.m5
y.m4
Rules
Clocks
Note: conflicts and orderings only arise between methods of the same module (like x.m1 and x.m2), not between methods of different modules (like y.m4 and x.m2)

---
Example: no conflict in either order
rule r1;
   x <= x + 1;
endrule
rule r2;
   y <= y + 2;
endrule
r2
r1
y._read
y._write
x._read
x._write
Rules
Clocks
There are no constraints between a method of x and method of y, so both rule orderings are legal (no conflict).
r1
x._read
x._write
r2
y._read
y._write
Rules
Clocks

---
Example: conflict in some schedules
rule r1;
   x <= y + 1;
endrule
rule r2;
   y <= y + 2;
endrule
<
r2
r1
>
y._read
y._write
y._read
x._write
Rules
Clocks
The only relevant constraint is: y._read < y._write
(there are no constraints between methods of different registers x and y).
The upper ordering (or schedule) is consistent with this (no conflict).
The lower ordering (or schedule) is inconsistent with this (has a conflict).
r1
y._read
x._write
r2
y._read
y._write
Rules
Clocks

---
Example: conflict in all schedules
rule r1;
   x <= y + 1;
endrule
rule r2;
   y <= x * 2;
endrule
r1
r2
>
<
y._read
x._write
x._read
y._write
Rules
Clocks
In both possible orderings, a method constraint is violated. This is a conflict.
r2
r1
>
<
x._read
y._write
y._read
x._write
Rules
Clocks
Compare slide 8: we had the same two actions in a single rule, and it was ok!
This illustrates that some Actions may be simultaneous (in a single rule)
but not concurrent (logically sequential in two different rules).

---
For conflicts, the earlier rule disables the later rule
A schedule (i.e., a particular linear ordering of rules) can contain conflicts.
A conflict between two rules in a schedule just means that the latter rule must be suppressed (not allowed to fire) if the earlier one fires.
r1 r2 r3 r5 rN
Suppose the compiler has picked this schedule of rules.
In this schedule, suppose there is a conflict between r3 and r5.
Then it generates logic like this: WILL_FIRE_r5 = (! WILL_FIRE_r3) && CAN_FIRE_r5
i.e., on those cycles that r3 fires, r5 is disabled.
Rule r5 can fire only on those cycles when r3 does not fire.